## Slide 1: Project Overview - Digital Logic Design - Hardware design using Verilog - Hardware Design for Elevator Control
Suraj Bidnur (PES University, Bangalore)
2018(June/July) – 1st Summer Break Intern Work

## Slide 2: Digital Logic Design
Basic Digital Design Elements / Function
Digital Design Fundamentals
Digital Chip Implementation

## Slide 3: Basic Digital Design Elements / Function
Transfer resistor and transistor
  Basic building block of any electronic circuit/device
  2 major uses: As a switch and as an amplifier
Logic Gates
  Eg: AND, OR, NOT, NAND, NOR, XOR, XNOR
  NAND and NOR are universal gates
    Any logic can be realised using either gate
Logic Optimisation Methods
  K-Maps, Quine-McCluskey
Storage Elements
  Flip-flops, Registers, Memory
    Memory realised using basic flip-flops

## Slide 4: Digital Design fundamentals
Threads
  A thread of execution or a set of instructions for a particular program
  Can be interlinked and can carry out data transfer
Finite State Machines
  Moore and Mealy
    Moore: Its output depends only on its current state
    Mealy: Its output depends not only on its current state but also the inputs provided

## Slide 5: Digital Chip Implementation
Full Custom
  Circuit design done with transistor level
  For high level performance, but cumbersome
  Analog design usually custom design
  Example: Intel – Processors, Memories
Semi Custom
  Uses standard cell design (pre-defined logic cells)
  Circuit design done using High level design language
  Gate Array (transistor arrays)
  Field Programmable Gate Array (FPGA)

## Slide 6: Elevator (Lift) Hardware control design
Requirement / Features
Assumptions / Limitations
Design Overview
Design verification
Hardware implementation using FPGA Platform (Altera DE2-70)
Results / Proto function

## Slide 7: Requirements / Features
3 floor design (can be extended to more floors)
External switches to call the Lift (up or down)
Internal switches to select which floor
All inputs debounced
External and internal lift calls are indicated by LED’s
Direction display (Up/Down)on 2 Seven-Segment displays
Floor number display on 1 Seven-Segment display

## Slide 8: Assumptions / Limitations
Due to less push buttons on the FPGA
  UP and DOWN external requests are done using only one push button
  One transition of the toggle switch is taken as one signal
To decide priority of the level calls, if the lift is moving up then it ignores the calls from the lower levels and vice versa

## Slide 9: Design Overview
This simple lift control system controls a lift which moves for 3 floors which are ground, first and second
3 push buttons are used to decide the external call for the direction of the lift
  For the 1st floor external call, 1 click-> UP, 2 clicks-> DOWN and 3 clicks-> BOTH
  Ground floor button is for UP and 2nd floor click is for DOWN
1 push button used to reset the system (active low reset)
3 switches are used to select the floor number which is the internal panel of the lift
All the inputs (switch and push-buttons) are debounced to prevent the glitches that generally occur when manual switches are pressed/toggled

## Slide 10: Design Overview
No derived clock is being used but instead a slow reference signal is used as an enable signal to all the logic elements
The external and internal lift calls are indicated with the help of LED’s which are activated on call and cleared by the lift
2 Seven-Segment displays are used to display the direction in which the lift is moving
  UP for UP and dn for DOWN
1 Seven-Segment display is used to display on the floor number where the lift is currently at
The movement of the lift is all controlled by a state machine

## Slide 11: Design Details
All the inputs (push-button and switch) are debounced
After debouncing the inputs, a pulse is generated for each transition which is used to control the state machine
Each input is sensed by the state machine and the appropriate state movement occurs
The lift moves to the next floor after a short period of time with the help of a counter
After a state movement, the state machine sends the output details to the output processing modules
These output processing modules take the signals from the state machine and produce the necessary outputs
Start
Processing inputs
State machine movement
Output and display
Stop

## Slide 12: State Machine Diagram
INITIAL
Reset active
LEVEL-0
Reset Withdrawn
LEVEL-1
Lvl-1/0 ext call
Lvl-1/0 int call
No action
No action
LEVEL-2
No action
Lvl-2/1 ext call
Lvl-2/1 int call
If reset
If reset
Lvl-0/2 ext call
Lvl-0/2 int call
If reset
Legend:
int-> internal
ext-> external

## Slide 13: Design Verification
The final design DUT (Device Under Test) verification was done through a verilog simulator
The testbench required for the simulation consists of all the instances of the required modules for the DUT
In the testbech, different input signals are passed and the outputs are observed for proper behaviour

## Slide 14: Design Verification
Test cases
  Reset- Test :
    When reset input is active the lift is at Level-0
    When Lift is at any other level, if reset is active lift will come to level-0
    No inputs are sensed when in reset
  External Up/Down Test
    If Lift is in other level, on Up/Down pushing Lift will come to the level where signal is sensed,
    Tested at each level’s Up/Down
  Lift Internal level Test
    Pushing the switches internal to the lift, will take to the level required based on switch pushed (Level 0/1/2)
    Tested at each level to go to any other level

## Slide 15: Design Verification
Reset Test

## Slide 16: Design Verification
External UP/DOWN Test

## Slide 17: Design Verification
Internal Level Test

## Slide 18: Design Verification
All Test Cases

## Slide 19: Hardware Implementation using FPGA Platform (Altera DE2-70 board)
DE2-70 FPGA Platform Overview
  Altera Cyclone II FPGA \w 70K Les
  Various input & output i/f to develop specific function
  Refer to following picture for features

## Slide 20: Hardware Implementation using FPGA Platform (Altera DE2-70 board)
Design was compiled and mapped to FPGA (Cyclone-II) on DE2-70 board
After code compilation, the required pin assignments are made using the board datasheet
  Pin assignment for push button, Toggle, LED & 7-Segment LED
After pin assignment is complete, the device is programmed. This causes the design to be burned on the FPGA so it can be implemented
When the programming is complete, the design can be tested using actual inputs from the board

## Slide 21: Hardware Implementation using FPGA Platform (Altera DE2-70 board)
Elevator (Lift) functioning (Add Picture & Video of possible)

## Slide 22: Result
I learnt the basics of digital electronics which includes logic gates, optimisation and finite state machines
Basics of digital logic design, implementation and testing using Verilog-HDL
And finally, demonstrated the learnings through a mini project with actual specific design function (Elevator Control Logic)
  Understanding the requirements of a specific design
  Designing the Logic for the specific function
  Testing the design in simulator and on FPGA platform

## Slide 23: Acknowledgement
I am very much thankful to Anuj Ramanujan Valmiki for imparting the knowledge on Basics of Digital design concepts, Hardware porting on FPGA and assisting me through out this process.